## Slide 1: Fading
Yan Fei

## Slide 2: Contents
Concepts
Cause of Fading
Slow and Fast Fading
Fading Models
Solution

## Slide 3: Concept
What is Fading?
  It is about the phenomenon of loss of signal in telecommunications.
  It refers to the distortion that a carrier-modulated telecommunication signal experiences over certain propagation media.
  A fading channel is a communication channel that experiences fading.
Notes: Multi-path effect means that a signal transmitted from a transmitter may have multiple copies traversing different paths to reach a receiver. Thus, at the receiver, the received signal should be the sum of all these multi-path signals. Because the paths traversed by these signals are different; some are longer and some are shorter. The one at the direction of light of signal (LOS) should be the shortest. These signals interact with each other. If signals are in phase, they would intensify the resultant signal; otherwise, the resultant signal is weakened due to out of phase. This phenomenon is called channel fading. In general, there are two criteria to measure channel fading, including (1) Doppler spread, and (2) delay spread.